Photomap generation

Content

Photomap generation	1

Content	1

Name:	1

Data:	1

1. Aim of the laboratory	2

2. Data	2

3. Data analysis	2

4. Photomap generation	2

Name:

Data:

Aim of the laboratory

The main aim of the laboratory is to be familliar with the fotomap generation .

Data

- Digital airborne image in scale 1:36 000, pixel size 6 m, 0.22 m in terrain : 4_6498_a

- Certification of camera calibration: wspolrzedne.doc

- DTM

- Ground Control Points: wspolrzedne.doc fotopunkty...-....jpg

- Roads, for accuracy assessment: drogi_77

Data analysis

Display  „4_6498_a.” in pixel coordinate system , analyse coordinate

Display DTM   see coordiante changes, compare values in right down and left upper part of the image.

Evaluate surface hights differences for area for photomap generation.  (ΔX = 1000 m, ΔY = 1000 m)

From: Xmin = 588 200 + 20m ( student’s number,

Ymin = 231 400 + 20m ( student’s number

Photomap generation

Georeference creation

    - Display „4_6498_a.”.

    - From display window File/Create/Georeference, Option: GeoRef Tiepoints, Coordinate System „ukl1992”, Sub-Pixel Precision.

    - transformation „Conformal”

    - Tools  click GCP, input  XY. Add 4 points

    - Coordinate differences  (DRow, DCol); calculate to terrain units [m] (pixel size in terrain = ?)

    - Confirm transformation

Photomap creation

    - From main ILWIS menu create the next georeference File/Create/Georeference, Georef Corners; Coordinate System „ukl1992”; piel size 0.2; size range like above, „Center of Corner pixels”.

    - Photomap creation, Operation-List, Resample;

Accuracy analysis

    - Display photomap

    - Layers - Add layer: „drogi_77” – correct road position. Measure  the distance between real road location and the location on the photomap (at least 20 points).  Calculate RMSE